NARAYANA ENGINEERING COLLEGE::NELLORE

### DEPARTMENT OF ELECTRONICS & COMMUNICATION ENGINEERING  Social Media Based   Home Automation

Details regarding project team members:

- 15711A0401     : A.Keerthi

- 15711A0430     : MD.Sayeeda Tasneem

- 15711A0404     : B.L.Pavani Charitha

- 15711A0431     : M.Honey Harshitha

- 15711A0429     : MD.Shazia

Report  about our project :

Home automation or domotics is building automation for a home, called a smart home or smart house. It involves the control and automation of lighting, heating (such as smart thermostats), ventilation, air conditioning (HVAC), and security, as well as home appliances such as washer/dryers, ovens or refrigerators/freezers.Wi-Fi is often used for remote monitoring and control. Home devices, when remotely monitored and controlled via the Internet, are an important constituent of the Internet of Things. Modern systems generally consist of switches and sensors connected to a central hub sometimes called a "gateway" from which the system is controlled with a user interface that is interacted either with a wall-mounted terminal, mobile phone software, tablet computer or a web interface, often but not always via Internet cloud services.

While there are many competing vendors, there are very few worldwide accepted industry standards and the smart home space is heavily fragmented.Manufacturers often prevent independent implementations by withholding documentation and by litigation.

The home automation market was worth US$5.77 billion in 2013, predicted to reach a market value of US$12.81 billion by the year 2020.

In this project first we had known about MINILAB.Then how to set up node MCU board .  Then interfacing Node MCU board with LEDS & RELAYS .Then configuring web server and client control LED via internet, We will make LEDs to BLINK using internet.Then download BLINK  APP in android mobile and we will develop the project using BLINK APP we registered in to the BLINK APP.Then using FB account in android mobile or in PC by updating status like TURN OFF LIGHTS & TURN ON LIGHTS we can control lights in our home from anywhere .By using bothBLINK APP and FB account lights were  turned  ON & OFF.Finally we tested and verified our project  on SOCIAL MEDIA based Home Automation i.e home appliances is controlled by using FB account and social media accounts.

Batch-mates with Project KIt