TAMILNADU STATE COUNCIL FOR SCIENCE AND TECHNOLOGY

DOTE  Campus, Chennai-600025

PROPOSAL FOR CONSIDERATION UNDER STUDENT PROJECTS SCHEME

SOLAR POWERED ELECTRIC WHEELCHAIR FOR CHILDREN WITH DISABILITY

submitted by

N.Arul kumar

S.Boopathy

A.S.Sangameswaran

Project Guide

Dr.B.Indu Rani

Department of Electrical and Electronics Engineering

Bannari Amman institute of technology

Sathyamangalam-638401

| FORMAT FOR STUDENT PROJECT PROPOSAL |
| --- |
| 1. Name of the Student (s) | N.Arul kumar,S.Boopathy,A.S.Sangameswaran. |
| one e-mail id | indurani@bitsathy.ac.in |
| 2 Name of the Guide | Dr.B.Indu Rani |
| Designation | Associate Professor |
| Institutional Address | Department of Electrical and Electronics Engineering Bannari Amman Institute of Technology Sathyamangalam,Erode-638401 indu_b04@yahoo.com |
| Phone No. & Mobile No. | 9790437302 |
| 3. Project Title | Solar Powered Electric Wheelchair for Children with Disability |
| 4. Sector in which your proposal is to be considered | Engineering & Technology |
| 5 Project Details | Enclosed in Annexure –I |
| 6 Has a similar project been carried out in your college / elsewhere. If so furnish details of the previous project and highlight the improvements suggested in the present one | Electric wheel chairs are available in market at a very high cost. In India, electric wheel chairs for school going children with disability are not affordable. Disabled children mostly depend on manual wheelchairs and other persons for their day to day movements. These wheelchairs are not suitable for outdoor use. Moreover, the children must use physical force to turn the wheels to change the direction. This action is physically stressful and can result in muscle and joint pain, torn rotor cuffs, repetitive stress injury and carpal tunnel syndrome; which causes secondary injury or further disability. In the proposed work, the wheel chair is designed to run in outdoors at a maximum speed of 25 km/h. For smoother operation, BLDC motors are used and the electronic control is made using a PIC microcontroller. The wheel chair is self driven, independent, user friendly and low cost. |

CERTIFICATE

This is to certify that Mr.N.Arul Kumar, Mr.S.Boopathy, Mr.A.S.Sangameswaran is a bonafide final year student of U.G.-Electrical and Electronics Engineering course of our college and it is also certified that two copies of utilization certificate and final report along with seminar paper will be sent to the Council after completion of the project by the end of April 2018.

Signature of the Guide 		Signature of the HOD 		              Signature of the Principal/

Head of the Institution

Annexure-I

Solar Powered Electric Wheelchair for Children with Disability

Introduction

First wheelchair model evolved long back in 18th century, but rapid development in this field initiated since mid of 20th century. Since then, many varieties of models had been designed, extending into broad range of products. Electric wheel chairs are available in market at a very high cost. In India, electric wheel chairs for school going children with disability are not affordable. This project involves the design of an economically designed electric wheelchair for children with disability.

Disabled children mostly depend on manual wheelchairs and other persons for their day to day movements. These wheelchairs are mostly not suitable for outdoor use. Moreover, the children must use physical force to turn the wheels to change the direction. This action is physically stressful and can result in muscle and joint pain, torn rotor cuffs, repetitive stress injury and carpal tunnel syndrome; which causes secondary injury or further disability. The wheel chair is a major hindrance to continue their education.

So it is necessary to develop a self driven, user friendly and a low cost wheel chair which can drive the children to schools. In the proposed work, the wheel chair is designed to run in outdoors at a maximum speed of 25 km/h. For smoother operation, BLDC motors are used and the electronic control is made using a microcontroller. Battery is used to supply the motor and electronic controllers. Solar panels are used to charge the battery in day time when the wheel chair remains idle in schools.

2. Objectives of the project

This project aims to redesign an circuit Wheelchair into a solar powered wheelchair. The ideal customer is a person living in a college/school campus or a resident of rush free premises. The objectives are to calculate the area of PV module, to replace the currently used lead-acid battery with a lighter and better one, to design the frame for mounting the module and to design the electric Circuit. The replacement of two or three lead-acid battery and estimation of power rating of PV module thus its weight goon simultaneously.

Fig.1. Block diagram of Solar Powered Wheel Chair

In the Block diagram solar PV panel are used for power supply using renewable resource and MPPT are track the maximum power from solar panel and stabilized the power equalized supply to the battery. There also external battery charger are also available for emergency charging , like wise unconditioned weather else use the vehicle in indoor areas not able to charge. Battery source given to motor drives , but the controller signal given by Ardunio. Joystick plays important role in wheelchair to controlled the chair position to any direction. And controlled the motor many relays are used to access the PMDC motor and also viber motor. Speedometer are connected calculate the speed of wheelchair.

Methodology

- Improved the specification of wheel chair

- Simulation the project in draw sheet.

- Design and Fabricate the wheel chair chassis , adjust the seating arrangement and calculate space for fitting of solar panel roof above the wheel chair.

- Developed the control circuit for controlled the electric motor and assembling.

- Testing the model in on road and check comfortability.

the design and implementation of low cost solar powered wheelchair for physically challenged people. At present the solar energy sector is growing like never before. PV is emerging as a major power resource, steadily becoming more affordable and proving to be more reliable than utilities. Photovoltaic power promises a brighter, cleaner future for next generation. The instances of solar powered vehicles have increased many a told in recent years. This project has been taken under the motivation of utilization of renewable and clean sources of energy.

This project aims to redesign a circuit Wheelchair into a solar powered wheelchair. The ideal customer is a person living in a college/school campus or a resident of rush free Premises. The objectives are to calculate the area of PV module, to reconnect the currently used Lead-acid battery with a lighter and better one for indoor usages, to design the frame for mounting the module and to design the electric Circuit. The replacement of the lead-acid battery and estimation of power rating of PV module thus its weight goon simultaneously. After finalizing these two PV module and battery are procured and frame for mounting the module is fabricated and finally the electric circuit is made. This project ensures use of solar energy to charge the battery and increased life of the wheelchair.

As we know that there are different types of components are available in market. The components we are using are brushed DC motor, Solar panel, Battery, charge controller throttle and joystick controller. Hand-powered tricycles are presently being used to provide mobility for disabled persons. With this project we designed and manufactured a system to convert the hand powered tricycle to an electric motor powered version. Solar- powered vehicles (SPVs) use photovoltaic (PV) cells to convert sunlight into electricity. The electricity goes either directly to an electric motor powering the vehicle, or to a special storage battery. PV cells produce electricity only when the sun is shining. Without sunlight, a solar powered car depends on electricity stored in its batteries. There are several types of tricycle that can be categories that is paddle tricycle, motorized tricycle, and electric tricycle. The weakness of the tricycle make people do not like to used tricycle. First, paddle tricycle needs a lot of energy to paddle the tricycle. Next, motorized tricycle that used fuel as it prime mover. The tricycle use fuel that is costly. Besides that, motorized tricycle will make pollution that can be very bad for our environment especially in this period that global warming happen to the earth. Lastly, electric tricycle that generate by battery can be only be sufficient for about an hour. The user needs to find power supply to recharge the battery or else they need to paddle the tricycle that used more energy compared to the normal tricycle because of the weight.

Work plan

| Activity | Duration in Months |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 |
| Literature survey |  |  |  |  |  |  |
| Design of wheel chair |  |  |  |  |  |  |
| Procurement of components |  |  |  |  |  |  |
| Fabrication of chassis and assembling. |  |  |  |  |  |  |
| Electric motor assembly in chassis |  |  |  |  |  |  |
| Implementation of controller in wheel chair. |  |  |  |  |  |  |
| Testing of wheelchair and final correction. |  |  |  |  |  |  |
| Report preparation |  |  |  |  |  |  |

Budget

| Sl.No | Component | Cost( in Rs) |
| --- | --- | --- |
| 1 | P PMDC Motor with its controller | 6000 |
| 2 | Viper Motor | 1500 |
| 3 | Steel rod | 2500 |
| 4 | wheels | 2500 |
| 5 | Ardunio controller set and relays | 1700 |
| 6 | Battery 12v 40ah | 5000 |
| 7 | Fabrication of power circuit- soldering, Steel welding, Grinding | 2000 |
| 8 | Miscellaneous | 1000 |
| 9 | Report | 300 |
|  | Total |  |

# Text boxes

DC-DC

CONVERTER

DC-DC

CONVERTER

SPEEDOMETER

JOYSTICK CONTROLLER SET

CONTROL SIGNAL FROM     ARDUNIO

ELECTRIC MOTOR

MOTOR CONTROLLER

MPPT

BATTERY BACKUP

SOLAR PV PANEL

EXTERNAL BATTERY CHARGER